http://www.inchem.org:80/documents/hsg/hsg/hsg026.htm

IPCS INTERNATIONAL PROGRAMME ON CHEMICAL SAFETY

Health and Safety Guide No. 26

PYRROLIZIDINE ALKALOIDS

HEALTH AND SAFETY GUIDE

UNITED NATIONS ENVIRONMENT PROGRAMME

INTERNATIONAL LABOUR ORGANISATION

WORLD HEALTH ORGANIZATION

WORLD HEALTH ORGANIZATION, GENEVA 1989

This is a companion volume to Environmental Health Criteria 80:

Pyrrolizidine Alkaloids.

Published by the World Health Organization for the International

Programme on Chemical Safety (a collaborative programme of the United

Nations Environment Programme, the International Labour Organisation,

and the World Health Organization)

This report contains the collective views of an international group of

experts and does not necessarily represent the decisions or the stated

policy of the United Nations Environment Programme, the International

Labour Organisation, or the World Health Organization

ISBN 92 4 154347 8

ISSN 0259-7268

The World Health Organization welcomes requests for permission to

reproduce or translate its publications, in part or in full.

Applications and enquiries should be addressed to the Office of

Publications, World Health Organization, Geneva, Switzerland, which

will be glad to provide the latest information on any changes made to

the text, plans for new editions, and reprints and translations

already available.

(c) World Health Organization 1989

Publications of the World Health Organization enjoy copyright

protection in accordance with the provisions of Protocol 2 of the

Universal Copyright Convention.  All rights reserved.

The designations employed and the presentation of the material in this

publication do not imply the expression of any opinion whatsoever on

the part of the Secretariat of the World Health Organization

concerning the legal status of any country, territory, city or area or

of its authorities, or concerning the delimitation of its frontiers or

boundaries.

The mention of specific companies or of certain manufacturers'

products does not imply that they are endorsed or recommended by the

World Health Organization in preference to others of a similar nature

that are not mentioned.  Errors and omissions excepted, the names of

proprietary products are distinguished by initial capital letters.

CONTENTS

INTRODUCTION

1. PRODUCT IDENTITY AND USES

1.1. Identity

1.2. Physical and chemical properties

1.3. Uses

2. SUMMARY AND EVALUATION

2.1. Human exposure to pyrrolizidine alkaloids

2.2. Metabolism and excretion

2.3. Effects on experimental animals

2.4. Effects on human health

2.5. Effects on the environment

3. RISK EVALUATION

4. PREVENTIVE MEASURES AND MEDICAL ADVICE

4.1. Main hazards for man and the environment

4.2. Prevention of PA poisoning

4.3. Advice to physicians

4.4. Precautionary measures to protect the environment and to

prevent disease

4.5. First aid

4.6. Medical management

5. CURRENT REGULATIONS, GUIDELINES, AND STANDARDS

INTRODUCTION

The Environmental Health Criteria (EHC) documents produced by the

International Programme on Chemical Safety include an assessment of

the effects on the environment and on human health of exposure to a

chemical or combination of chemicals, or physical or biological

agents. They also provide guidelines for setting exposure limits.

The purpose of a Health and Safety Guide is to facilitate the

application of these guidelines in national chemical safety

programmes. The first three sections of a Health and Safety Guide

highlight the relevant technical information in the corresponding EHC.

Section 4 includes advice on preventive and protective measures.

The target readership includes occupational health services, those in

ministries, governmental agencies, industry, and trade unions who are

involved in the safe use of chemicals and the avoidance of

environmental health hazards, and those wanting more information on

this topic. An attempt has been made to use only terms that will be

familiar to the intended user. However, sections 1 and 2 inevitably

contain some technical terms. Further background information on the

subject of this Guide may be found in Environmental Health Criteria

80:  Pyrrolizidine Alkaloids.

Revision of the information in this Guide will take place in due

course, and the eventual aim is to use standardized terminology.

Comments on any difficulties encountered in using the Guide would be

very helpful and should be addressed to:

The Manager

International Programme on Chemical Safety

Division of Environmental Health

World Health Organization

1211 Geneva 27

Switzerland

THE INFORMATION IN THIS GUIDE SHOULD BE CONSIDERED AS A STARTING POINT

TO A COMPREHENSIVE HEALTH AND SAFETY PROGRAMME

1.  PRODUCT IDENTITY AND USES

1.1  Identity

The toxic pyrrolizidine alkaloids (PAs) are a large group of related

compounds (about 160 are known) that occur in plants, mainly in

species of  Crotalaria (Leguminosae),  Senecio and related genera

(Compositae),  Heliotropium, Trichodesma, Symphytum, Echium, and

other genera of the Boraginaceae. The chemical structures of some

alkaloids that are important in relation to human disease are shown

below.

1.2  Physical and Chemical Properties

The pure alkaloids are mostly crystalline solids; some are gums or

amorphous solids. Some are only slightly soluble in water, but all

dissolve when neutralized with acid. They occur in the plants partly

as  N-oxides, which are water soluble. The alkaloids are fairly

stable, but are subject to hydrolysis in alkaline solution and to

enzymatic decomposition. The latter occurs in some plant species

during wilting and drying. The stability of the alkaloids when the

plants are cooked is not known.

1.3  Uses

One alkaloid, monocrotaline, is marketed commercially as a fine

chemical for research purposes. Another, indicine  N-oxide, is being

tested as an antitumour drug in human beings.

2.  SUMMARY AND CONCLUSIONS

2.1  Human Exposure to Pyrrolizidine Alkaloids

The contamination of cereal grains with seeds of PA-containing plants

has caused epidemics of human poisoning in four countries. The plants

involved were species of  Heliotropium, Trichodesma, Crotalaria, and

Senecio. Some of these plants thrive under arid conditions and their

growth may be favoured by drought. Another important form of exposure

is the use of PA-containing herbs as medicines, food, or beverages;

this has resulted in occasional cases of human poisoning. The most

important of such PA-containing plants are  species of Heliotropium,

Crotalaria, Senecio, and  Symphytum. Symphytum species (comfrey)

are also available in the form of ointments or as digestive aids in

the form of capsules.

Low-level exposure may occur in some countries through the presence of

PAs in foods, such as honey and milk, but no reports of human

poisoning caused through these media are available.

2.2  Metabolism and Excretion

PAs are readily absorbed from the digestive tract and cause harmful

effects only after undergoing activation in the liver to toxic

metabolites. Effects include a variety of changes leading to permanent

damage to genes and chromosomes, the ability of the cells to divide,

or to the development of cancer, and even cell death. The alkaloids

are quickly converted to harmless compounds and are largely cleared

from the body within a few hours of absorption, so that no traces of

the ingested PAs or their breakdown products are detectable in the

body tissues and fluids. There are no indications that the alkaloids

themselves accumulate in animal tissues, but their effects are

cumulative, even at low rates of intake. The proportion excreted in

urine varies according to the water solubility of the alkaloid.

Estimates of the total intake over a long period can only be

approximate.

2.3  Effects on Experimental Animals

The acute toxicity of PAs varies widely. The rat LD50s of most

alkaloids known to be significant for human health are in the range of

34-300 mg/kg, though some approach 1000 mg/kg. When ingested, the

toxicity of the  N-oxide of an alkaloid is similar to that of the

parent alkaloid.

PAs are toxic for a wide variety of domestic, laboratory, and farm

animals, pigs and poultry being the most sensitive of farm animals

followed by horses and cattle, and sheep and goats, which are the most

resistant; sheep and goats are affected only after extended periods of

exposure.

The toxic effects of most PAs occur primarily and mainly in the liver.

Some PAs are particularly prone to cause damage in the lungs,

principally to the blood vessels, resulting in a rise in blood

pressure in the lungs, which leads to secondary effects on the

functioning of the right side of the heart. The kidneys and some other

organs are less commonly affected. The brain is the principal target

organ of one or two PAs.

The effects of PAs in animals may be acute or chronic, depending on

the dose level and the period of survival after exposure. In acute

poisoning, death occurs within about 7 days, due to severe liver

damage. Chronic liver damage may follow administration of a single

sublethal dose or of repeated low doses.

PAs produce aberrations in the chromosomes in plant and mammalian

cells and induce changes in genes that are perpetuated in subsequent

cell divisions in mutagenesis test systems. Several PAs have been

shown to be capable of producing cancer, chiefly in the liver in rats.

2.4  Effects on Human Health

Although all age groups are affected, children are particularly

vulnerable to the effects of PAs. The symptoms, which are generally

acute in onset, are characterized by upper abdominal discomfort that

develops rapidly and progresses to swelling of the abdomen resulting

in increased girth, sometimes accompanied by a reduction in the

quantity of urine excreted and swelling of the feet. The disease is

called veno-occlusive disease (VOD) because of the characteristic

obstruction of the small venous blood channels that carry blood from

the liver back to the heart. The disease often progresses rapidly and

mortality is high. There may be vomiting of blood in advanced stages

of the disease. While many patients recover, the disease may continue

for a long time in others resulting in a severely scarred liver - a

condition called cirrhosis. Some patients may have only vague symptoms

and the only sign of the disease may be persistent enlargement of the

liver.

The liver is usually the target organ but, in an epidemic caused by

contamination of the staple cereal with the seeds of  Trichodesma,

the brain and the nervous system were mainly affected.

Chromosome aberrations have been reported in the blood cells of

children affected by VOD but, as yet, there is no evidence pointing to

an increased incidence of cancer of the liver or other organs or

congenital anomalies in the newborn offspring of patients exposed to

PAs.

2.5  Effects on the Environment

Plants containing PAs are likely to grow as weeds among staple food

crops and pastures, especially following drought, and consumption of

such crops can cause large scale outbreaks of toxic disease in both

man and farm animals. Little is known about the effects on wildlife

but, in one report, the death of deer was ascribed to their grazing on

toxic plants.

PAs are believed to be biodegradable so that water supplies are not

suspect.

3.  RISK EVALUATION

No-observed-adverse-effect levels have not been established in

experimental animal studies with PAs. Estimates of intakes causing

toxic effects in human beings indicate that they are more sensitive

than rats and domestic animals. Rats dosed with lasiocarpine at a rate

equivalent to 0.2 mg/kg body weight per day (equivalent to about

2 mg/kg in the diet) developed tumours. Pigs fed monocrotaline at

1.8 mg/kg of feed (equivalent to about 0.08 mg/kg body weight per day)

developed chronic liver damage in several months. The lowest intake

rate causing VOD in a human being was estimated to be 0.015 mg/kg body

weight per day, and was the result of self-medication with a comfrey

preparation. In view of the established ability of some PAs to produce

cancer in rats, plant products containing them should not be eaten or

drunk.

4.  PREVENTIVE MEASURES AND MEDICAL ADVICE

4.1  Main Hazards for Man and the Environment

Consumption of contaminated grain or the use of PA-containing plants

as herbal medicines, beverages, or food by man, or grazing on

contaminated pastures by animals, may cause acute or chronic disease.

The principal target organ in man and most animals is the liver,

resulting in collection of fluid in the abdomen and swelling of feet,

etc. In experimental animals, administration of PAs has been known to

produce cancer. Though there is no proof yet of cancer developing in

man, such a possibility cannot be entirely ruled out.

4.2  Prevention of PA Poisoning

Prevention of exposure is the only effective method of limiting

toxicity due to PAs. Even low doses over a period of time may present

a health risk and exposure should be avoided or minimized as far as

possible. Measures are required at several action points.

4.3  Advice to Physicians

Occurrence of symptoms of rapidly increasing swelling of the abdomen

accompanied by dragging discomfort in the right upper abdomen,

particularly if affecting more than one member of the family or

several members of a community over a limited period and geographical

area, should arouse suspicion. The diet of such persons should be

examined for possible contamination with the seeds of toxic plants and

the affected persons should be questioned regarding the possible

intake of herbal preparations. If any such history is positive, the

suspected toxic seeds/herbs should be analysed for the presence of PAs

using a simple field test, which can be carried out in a not too

highly specialized chemical laboratory.

Examination of the liver by needle biopsy in patients or at post-

mortem examination is most likely to provide the crucial clue.

Haemorrhagic centrilobular necrosis and occlusion of the hepatic vein

radicles in the liver are the hallmarks of the disease, if found in

patients with the symptoms described above. Needle biopsy of the liver

should be performed only in a properly equipped hospital with

facilities for blood transfusion.

4.4  Precautionary Measures to Protect the Environment and to Prevent

Disease

(a) Toxic PA-containing flora growing in the region, particularly

those that may contaminate cereal grain crops, and those that are used

locally as herbal foods, beverages, or medicines, whether grown

locally or imported, should be identified.

(b) Appropriate agrotechnical practices should be followed for the

prevention/control of the growth of PA-containing plants among cereal

food crops and pastures.

(c) Appropriate systems should be developed for the routine monitoring

of seed grain and harvested grain crops to detect the presence of

PA-containing plants and seeds.

(d) If the crop is found to be contaminated, immediate steps should be

taken to remove the toxic plants from the fields and to rid the

domestic and commercial cereal grain stores of the toxic seeds by

sieving or winnowing and destroying the toxic seeds/plants.

(e) The suspected contaminant and its toxic PAs should be identified

in specialized laboratories.

(f) Public awareness of the risks arising from the consumption of

grain contaminated by seeds, and the use of herbal preparations

containing PAs as food or medicines, should be created through the

media.

(g) The import and sale of seeds, herbs, and herbal preparations

containing PAs should be restricted.

(h) In the event of an outbreak, epidemiological investigations of the

affected population should be carried out, and plans made for long-

term follow-up.

(i) Cases of PA poisoning should be recorded and surveillance

organized by Poison Control Centres or other appropriate agencies of

the government.

4.5  First Aid

Immediate first aid measures are rarely possible for an acute exposure

but may be required in the management of emergencies, such as vomiting

of blood from bleeding blood vessels in the oesophagus.

No specific antidote is known for PA-induced toxic effects. The only

immediate valuable measure is to:

- identify the source of the PA and

- STOP any continued exposure.

4.6  Medical Management

No specific antidote or therapy for PA toxicity is known. Treatment is

supportive.

5.  CURRENT REGULATIONS, GUIDELINES AND STANDARDS

COUNTRY        RESTRICTED ITEM                  NATURE OF RESTRICTION

Australia      Symphytum (comfrey)              Scheduled as a poison,

(Any part of the dried           effectively preventing sale

plant and its extracts or        for medicinal purposes

preparations for human

internal use)

Austria        Senecio numorensis               Medicinal preparation must

Symphytum officinale             be registered with the

Petasites officinalis            Federal Ministry of Health

Tussilago farfara                and Environmental Protection

Pulmonaria officinalis           and sold only in pharmacies

(used as medicinal

preparations)

Canada         Senecio jacobaea (ragwort)       Proposed for inclusion in

Symphytum asperum Lepech         the list of adulterants, thus

(prickly comfrey)                prohibiting sale of such

Symphytum officinale L.          compounds in or as food

root (common comfrey)            (Section B.01.046 of the

Symphytum x uplandicum           Canadian Food and Drug

Nym. (Russian comfrey)           Regulations)

Echimidine or any of its         Proposed for inclusion in

salts or any of the following    the list of adulterants, thus

plant species or extracts        prohibiting sale of these

or tinctures thereof:            substances in or as drugs

(Section C.01.038 of the

(i) Symphytum asperum            Canadian Food and Drug

(ii) Symphytum x uplandicum      Regulations)

(iii) Any other plant species

containing echimidine

Indonesia      Symphytum officinale L.          Dispensaries and drug stores

or its parts either fresh        not allowed to prepare, sell,

or dried                         or advertise it

USA            Crotalaria spectabilis           Compliance policy guidelines

Crotalaria sagittalis            require that the presence of an

Crotalaria striata               average of at least one whole

seed per pound of product

represents the criterion for

direct reference seizure to

the office of regulatory

affairs (ORA)HFC-25 and

for direct citation by the

district offices (OB/01/82)

COUNTRY        RESTRICTED ITEM                  NATURE OF RESTRICTION

Lasiocarpine                     Any solid waste (except

domestic) containing

lasiocarpine must be listed

as hazardous waste (subject

to regulation and

notification requirements);

where lasiocarpine is a

principal organic hazardous

constituent in the EPA

permit, incineration must

achieve a destruction and

removal efficiency of 99.99%

USSR           Stored grain:                    Contamination limit

Heliotropium lasiocarpum

-Seed                            0.1%

Trichodesma incanum

-Seed                            0%

-Seed grain                      Contamination with both

species is prohibited

(Note: It has been calculated that

0.1% tolerance for  H. lasiocarpum

seeds in stored grain could result in

1.82 mg of PA per kg of stored wheat)

Note: Besides the above, a number of countries have regulatory proposals under

development and several others enforce administrative or compliance guidelines

based on general prohibitory provisions for the basic food and drug products;

studies are being carried out to further evaluate the risk.

See Also:

Toxicological Abbreviations

Pyrrolizidine alkaloids (EHC 80, 1988)